Ball Labyrinth
Final Project
Ball Labyrinth

---
Introduction
- OpenGL
- SDL2
- GLM

---
Physics Model
- 3D rigid body model
- Ball represented as center with radius
- Walls represented as boxes with infinite mass
- Symplectic Euler used as update step
- Simple ball rolling:
  - No torque
  - No slip on the surface assumed

---
Rolling Ball
Angular momentum can be seen as reduced force acting on the ball
E_tot = {m v^2} over {2} + {I %omega^2} over {2}
I= {2 m R^2} over {5}
E_tot=E_kin+E_rot
E_tot = {m v^2} over {2} + {m v^2 R^2} over {5 R^2}
m g h = {m v^2} over {2} + {m v^2} over {5}
g h = {7 v^2} over {5}
Rolling
Sliding
v = sqrt{ {5} over {7} g h}
v = sqrt{ 2 g h}

---
Rolling friction
- Friction is a constant force dependent on the normal force to the surface
F_r = %mu F_N

---
AABB collision detection
- AABB boxes used to model the maze and floor
- Sphere to AABB collision detection
https://developer.mozilla.org/en-US/docs/Games/Techniques/3D_collision_detection/Bounding_volume_collision_detection_with_THREE.js

---
Collision Steps
- Detect if distance to
  centerpoint < radius
- Move ball outside of the collision box
- Update velocity according to rigid body model

---
Maze Generation
- Random automatic maze generation
  http://www.thingiverse.com/thing:24604
- Python script generates openscad file and .txt file with AABB boxes
- Openscad → generates .stl
- Blender → .obj from .stl
- Tiny Obj Loader used to import the .obj maze